## Slide 1
SAOA Consulting
NovaStar MX (COEX)
SIMPL+ Control Module for Crestron 4-Series
Seamless TCP/IP control of NovaStar LED processors — right inside your Crestron ecosystem.
Release 2.20.1 • saoa.se • info@saoa.se

## Slide 2
THE CHALLENGE
LED Walls are Complex
NovaStar processors require a proprietary TCP/IP API on port 8001 — not standard AV control.
Integration Gaps
Most AV control systems lack native NovaStar support, forcing custom workarounds.
Operator Friction
Without proper control, technicians must use separate software to manage presets, brightness and display mode.

## Slide 3
THE SOLUTION
NovaStar MX SIMPL+ Module
A ready-to-use SIMPL+ module that bridges Crestron 4-Series processors directly to NovaStar MX30 LED controllers over TCP/IP.
One-click Deploy
Drop the module into any SIMPL Windows project.
Full API Coverage
Presets, brightness, display mode & feedback.
Real-time Feedback
Live status back into your Crestron UI.
Zero Custom Code
No C# or raw TCP scripting required.

## Slide 4
KEY FEATURES
Preset Recall
Instantly recall up to 10 named presets stored on the NovaStar controller via a single analog signal.
Brightness Control
Smooth 0–100 analog brightness control with live feedback to the touch panel.
Picture Mute/UnMute
One-touch mute of the LED wall — ideal for presentations and AV events.
Display Mode Query
Request and display the current operating mode as a readable string feedback.
TCP Auto-Reconnect
Built-in heartbeat and recovery ensures the connection stays alive unattended.
Preset Name Strings
Fetches and exposes all preset names (1–10) as string signals for dynamic UI labels.

## Slide 5
SIGNAL REFERENCE
Inputs
Outputs / Feedback
Signal
Type
Description
Signal
Type
Description
Controller_IP$
String
IP address of NovaStar controller
Controller_Port
Analog
TCP port (default 8001)
Get_Display_Mode
Digital
Request current display mode
Picture_Mute
Digital
Mute LED wall output
Picture_UnMute
Digital
Unmute LED wall output
Get_Presets
Digital
Fetch preset names
Set_Brightness
Analog
Brightness 0–100
Set_Preset
Analog
Recall preset 1–10
DisplayMode_FB$
String
Current display mode text
Brightness_FB
Analog
Live brightness value
PresetActive
Analog
Currently active preset number
PresetName$[1-10]
String
Preset names from controller

## Slide 6
SYSTEM REQUIREMENTS
Crestron Processor
4-Series (CP4, MC4 or equivalent) Not designed for 3-Series
Firmware
Crestron firmware v2.0 or newer
SIMPL Windows
Version 4.17.00 or later
Network
TCP port 8001 open between the Crestron processor and NovaStar unit
NovaStar Hardware
MX30 controller (COEX platform) Firmware compatible with COEX API
This module is a drop-in SIMPL+ component — no additional middleware, servers or drivers required.

## Slide 7
WHY SAOA CONSULTING
Your AV integration specialist.
Crestron Certified
Deep expertise in SIMPL, SIMPL# and 4-Series architecture.
NovaStar Specialists
Direct experience with COEX API integration across live events and permanent installs.
Full Lifecycle Support
From design and programming to commissioning and on-site support.
Custom Development
Need a tailored module or full system design? We deliver.

## Slide 8
PROVEN TRACK RECORD
v2.1
Nov 2025
Initial public release of the NovaStar MX COEX module.
v2.20
Jan 2026
Major stability update: improved MX30 state handling, heartbeat monitoring and connection recovery.
v2.20.1
Apr 2026
Packaging cleanup: removed unused dependencies, reduced compiled .clz size from 3.8 MB to 1.4 MB.
Actively maintained with a clear versioning policy and backward-compatible upgrades.

## Slide 9
READY TO INTEGRATE?
Get the NovaStar MX SIMPL+ module working in your project today.
Contact Us
SAOA Consulting
info@saoa.se
https://saoa.se
Release 2.20.1 • Crestron 4-Series • TCP/IP • NovaStar COEX API